## Slide 1: Multi-Node ROS Application for Robotic Platform
Developed by
Pooya Nasiri and Arash A. Malekshah

## Slide 2: Project Overview
In this project, we focused on three main tasks: navigation, object detection, and manipulation. We developed a modular system with distinct nodes for each task, ensuring seamless communication via ROS.

## Slide 3: Project Objectives
The primary objectives of this project were to develop robust navigation, object detection, and manipulation systems for a robotic platform. We aimed to ensure stable communication between nodes and efficient task execution.

## Slide 4: System Architecture
Our system is designed with a modular architecture, which enhances code clarity and maintainability. Each node performs distinct tasks, which we will see in detail.

## Slide 5: Three nodes
Node A: Responsible for navigation and obstacle avoidance.
Node B: Focuses on object detection using AprilTags.
Node C: Handles object manipulation and placement.

## Slide 6: System Architecture
nodeA.cpp
MyActionServer.cpp
nodeB.cpp
nodeC.cpp
action
action
action
msg
msg
Human_node.cpp
srv

## Slide 7: Node A - Navigation and Obstacle Avoidance
Node A, implemented in nodeA.cpp, is responsible for guiding the robot to specific poses and avoiding obstacles. This node includes a custom ServiceClient for dynamic obstacle detection and uses MoveIt! to adjust the robot's torso height for optimal object detection.

## Slide 8: Node A Implementation Details
Key implementation steps for Node A include setting up the service client, managing navigation goals, handling obstacle avoidance, adjusting the robot's torso and head positions, and coordinating with Node B.

## Slide 9: Node A - Navigation Overview
Node A's primary objective is to guide the robot to a designated pose using custom services and action clients for navigation and obstacle avoidance.

## Slide 10: Obstacle Detection and Navigation
Node A includes a ServiceClient for obstacle detection, which manages dynamic obstacles during navigation. Challenges such as navigating around cylindrical obstacles are addressed using partial pose adjustments.

## Slide 11: Adjusting Torso Height with MoveIt!
The node optimizes object detection by adjusting the robot’s torso height using MoveIt!. This ensures the camera has the best possible view of the objects.

## Slide 12: Head Movement and ROS Communication
A HeadMover class is used to manipulate the robot’s head position, enhancing object detection accuracy. Several ROS publishers and message handlers coordinate the detection process.

## Slide 13: Completion Signal to Node B
After completing its tasks, Node A sends a signal to Node B to commence its operations, ensuring synchronized task execution.

## Slide 14: Node B - Object Detection
Node B is responsible for identifying and localizing objects using AprilTag detections. This node processes visual information from the robot’s camera and communicates the results to Node C for manipulation tasks.

## Slide 15: AprilTag Detection and Callback
Node B subscribes to tag detections to receive AprilTag detections, ensuring robust object identification and localization. The tagCallback function transforms detected poses into the global map frame, accurately mapping object positions.

## Slide 16: Coordination and Multi-View Detection
Node B waits for a signal from Node A to begin detection, ensuring the robot is properly positioned. It employs a multi-view strategy to ensure comprehensive object detection across different viewpoints.

## Slide 17: Data Preparation for Node C
Finalized object information is encapsulated in pick_info messages for Node C, facilitating precise object manipulation tasks.

## Slide 18: Node C - Object Manipulation
Node C handles the manipulation and placement of objects identified by Node B. It processes object coordinates and pick order from Node B and sets up a planning scene interface to ensure collision-free manipulation.

## Slide 19: Pick-and-Place Cycle
Node C executes a pick-and-place cycle involving transforming coordinates, positioning the end effector, attaching and lifting objects, transporting them, and placing them using laser scan data for accurate table detection.

## Slide 20: Laser Scan and Table Detection
The node uses laser scan data to detect and locate tables in the room, converting polar coordinates to Cartesian for accurate positioning.

## Slide 21: Communication between MyControlLaw and MyActionServer

## Slide 22: Achievements and Future Work
In conclusion, we successfully developed a modular, efficient system for robotic navigation, object detection, and manipulation. Future work could include enhancements to the object detection algorithms and broader applications of the system in different environments.

## Slide 23: Questions
Thank you for your attention.